## Slide 1: [Ref] SX-Aurora performance for seismic imaging
SX-Aurora shows good performance and performance/Watt vs other platforms in trials using proprietary seismic application of an industry-leading oil company
  X86: dual socket Skylake 6148 (2x 20 cores @ 2.4GHz), Power measurement using IPMI information
  NVIDIA V100 PCIe 32GB – OpenACC, power measurement using nvidia-smi
  SX-Aurora TSUBASA Vector Engine (8 cores @ 1.4GHz), power measurement using vecmd(VE card command)
Chart: 
| Acoustic (kernel +MPI part only) | Elastic (kernel + MPI part only)
x86 | 1 | 1
V100 | 2.13 | 2.65
SX-Aurora | 2.65 | 3.5
Acoustic
(kernel + MPI part only)
Elastic
(kernel + MPI part only)
Chart: 
| Acoustic (kernel +MPI part only) | Elastic (kernel + MPI part only)
x86 | 1 | 1
V100 | 1.69 | 2.04
SX-Aurora | 2.09 | 2.8
Acoustic
(kernel + MPI part only)
Elastic
(kernel + MPI part only)
Performance (normalized against x86)
Performance per Watt (normalized against x86)

## Slide 2: [Ref] configuration
  X86: dual socket Skylake 6148 (2x 20 cores @ 2.4GHz)
  Executed binary optimized by customer(oil & gas company)
  Compiled with Intel compiler
  Using IPMI information for power consumption
  NVIDIA V100 PCIe 32GB
  Open ACC code provided by customer (Oil & Gas company)
  No CUDA coding
  Compiled with PGI compiler
  Using nvidia-smi to measure power consumption
  SX-Aurora TSUBASA Vector Engine (8 cores@1.4GHz)
  Source code tuned by NEC
  Compiled with NEC compiler
  Using vecmd (ve card command) to measure power consumption